## Slide 1: inline PHY acceleration: a gpu based solution for o-ran
Lopamudra Kundu (Lopa) 02/06/2020

## Slide 2: purpose
Introduction of inline PHY acceleration model to O-RAN, with end-to-end high PHY implementation on GPU as one example.

## Slide 3: agenda
Introduction: O-DU high-PHY deployment options:
  Lookaside acceleration approach.
  Inline acceleration approach.
GPU based inline acceleration architecture.
Proposals.

## Slide 4: O-DU deployment
PHY acceleration options
Lookaside PHY acceleration
  Most of the functional blocks of O-DU high-PHY are processed by CPU.
  A subset of PHY layer algorithms is offloaded to accelerator (FPGA/GPU).
Inline PHY acceleration
  End-to-end O-DU high-PHY pipeline is implemented on accelerator.
  GPU is an ideal candidate for SW defined inline acceleration.

## Slide 5: GPU based inline phy acceleration
Example: 5G PDSCH/PUSCH pipeline
Processing of end-to-end high-PHY functional blocks on GPU enables “inline” PHY acceleration.
GPU accelerated PHY can scale with evolving 5G requirements due to GPU’s programmability, agility and capability of massive parallel computation.

## Slide 6: Proposals
Introduce inline acceleration based on end-to-end high-PHY implementation on accelerator (e.g., GPU) as one option for O-DU PHY algorithm acceleration.
Introduce an AAL profile based on end-to-end high-PHY acceleration.