## Slide 1: AAL API for inline acceleration
06/18/2020

## Slide 2: agenda
AAL Architecture for Inline Profile
Scope of AAL
  Execution Model
  Buffer Management
AAL API functions
  Discover, Initialize, Configure, Enqueue and Dequeue
Example of Enqueue and Dequeue
  Uplink
  Downlink

## Slide 3: Aal architecture for inline profile
For inline profile, Acceleration Abstraction Layer (AAL) interfaces between L2 adapter and HW accelerator.
AAL interacts with HW accelerator through the following set of APIs:
  Discover
  Initialize
  Configure
  Enqueue
  Dequeue
NIC
L2 + Application SW
GPU
Enqueue
Dequeue
Configure
Initialize
L2 <-> L1 interface*
*e.g. FAPI
PHY Driver
CUDA Driver
FH Driver
User space Software
Kernel space
discover
AAL
L2 adapter

## Slide 4: Scopes of aal
Execution model and buffer management
Workload execution
Multiple workloads (i.e. PHY pipelines) can be launched in parallel on a HW device.
No ordering restriction is imposed on completions of workloads submitted concurrently.
Priority among multiple workloads can be handled by assigning a priority value to each workload.
  The priority value can be based on type of profile (e.g. PUSCH vs. PDSCH) or type of service (eMBB vs. URLLC).
Buffer management
AAL does not handle data I/O buffer management for inline profile.
  L2+ application assigns the buffers and the buffer pointer is passed through AAL during enqueuing PHY workload.
  PHY driver is responsible for managing data I/O between CPU and GPU.
  FH driver is responsible for managing I/O between GPU and NIC using GPU DPDK.

## Slide 5: Discover and Initialize
ORAN_AAL_discover
Description
  Get information about available physical devices and their properties.
    Example: device management functions of the CUDA runtime API (e.g. cudaGetDeviceProperties, cudaDeviceGetCount) can be used to get GPU related information.
  The function would return a pre-defined data structure populated with device related information (e.g., number of devices, device id, device name, AAL profile).
Device
Cell
Task
…
AAL context
ORAN_AAL_init
Description
  Create AAL context with a set of objects that can be queried and configured by AAL, e.g. device list, cell list, task list etc.
  The function returns a pointer (*ctx_h) to the location of AAL Context (Context).

## Slide 6: configure
ORAN_AAL_obj_create/get/set/destroy
Key input parameters
  *ctx_h : Pointer to the AAL Context.
  void* obj_info : parameters needed to configure an object (e.g. cell).
  int obj_name: name of the object to be configured (e.g. cell).
Description
  A set of functions providing a control mechanism for managing objects internal to AAL.
  The input parameters to the function call depends on the object type to be configured.
ORAN_AAL_obj_create | Create a new obj within AAL context, e.g. a new cell
ORAN_AAL_obj_get | Query to know the status and attributes of an object, e.g. the cell configurations
ORAN_AAL_obj_set | Change the state of an object, e.g. activate or deactivate a cell
ORAN_AAL_obj_destroy | Destroy an object from AAL context, e.g. delete a cell object from AAL Context

## Slide 7: Enqueue and dequeue
ORAN_AAL_inline_enqueue
Key Input parameters
  *ctx_h : Pointer to the AAL Context (Context).
  struct slot_command: parameters needed to process UL/DL PHY pipeline and buffer pointer for data I/O.
Description
  L2 adapter submits one or multiple PHY workload(s) to AAL through this function.
    In case of multiple workloads submitted concurrently, priority can be attached to each workload.
    For parallel execution of multiple workloads, the completion or response can be out-of-order.
ORAN_AAL_inline_dequeue
Key Input parameters
  int task_id: enqueued task identifier, that was provided by L2 adapter as a part of slot_command in the enqueue function.
Description
  L2 adapter invokes dequeue function to check the status of execution completion.
  The function would return the completion status to the application.

## Slide 8: Example of Enqueue and dequeue: uplink
Example of UL pipeline enqueued by L2 adapter
Once L2 adapter enqueues an UL task, PHY driver triggers a series of steps to-
  Prepare UL subtasks to be executed sequentially to process UL pipeline.
  Instruct GPU to prepare for launching UL PHY pipeline.
  Send C-plane msg. to FH driver.
  Initiate U-plane data reception in GPU.
  Once UL PHY execution is complete, get results from GPU, including status, statistics and PHY execution outcome.
L2 adapter invokes dequeue function to check for completion status.
L2 adapter
PHY driver
ORAN_AAL_inline_enqueue
Send C-plane msg.
FH driver
cuPHY <-> GPU
Receive U-plane data
launch_UL_PHY
Status, statistics, PHY execution outcome
Prepare UL tasks
Polling for event
L2 adapter
PHY driver
FH driver
cuPHY <-> GPU
ORAN_AAL_inline_dequeue
Completion status
AAL
AAL

## Slide 9: Example of Enqueue and dequeue: downlink
Example of DL pipeline enqueued by L2 adapter
Once L2 adapter enqueues a DL task, PHY driver triggers a series of steps to-
  Prepare DL subtasks to be executed sequentially to process DL PHY pipeline.
  Launch DL PHY pipeline on GPU.
  Upon PHY execution completion, trigger FH driver for sending C-plane msg.
  Trigger FH driver for sending U-plane msg.
L2 adapter invokes dequeue function to check for completion status.
L2 adapter
PHY Driver
ORAN_AAL_inline_enqueue
FH driver
cuPHY <-> GPU
launch_DL_PHY
ORAN_AAL_inline_dequeue
Send C-plane msg.
Prepare DL tasks
L2 adapter
PHY Driver
FH driver
cuPHY <-> GPU
Send U-plane msg.
Completion status
Polling for event
AAL
AAL