## Slide 1: AAL Interface (AALI): definition & implementation
Lopamudra Kundu (Lopa) and Elena Agostini
02/03/2021

## Slide 2: agenda
Scope of the AAL Interface (AALI)
  Definition & Implementation
AALI implementation options
  Gap analysis between DPDK BBDEV API and Inline Acceleration API
Conclusion

## Slide 3: Scope of AAL Interface (AALI)
AALI Definition[1]
“The AAL specification shall define the AALI – the interface between the application and hardware accelerator in the O-Cloud instance. This includes the APIs and information models used by the application to interface with the AAL implementation.”
AALI Implementation[1]
“The AALI implementation itself shall not be defined by the AAL specification and is up to individual vendors to realize and can be implementation specific.”
Definition and Implementation
Application
HW accelerator
AAL implementation
(vendor specific)
O-RAN Cloudified Network Function
SW Libraries & Drivers
O-Cloud Node
AALI
Fig. 1 AAL Interface
[1] O-RAN WG6 AAL GAnP Spec.v01.00
Proposal 1:
O-RAN shall define AALI API in terms of Requirement, AAL profiles, Operations and Information/data model.
AALI API definition should not be guided by a specific AALI implementation.

## Slide 4: AALI API implementation
AALI reference implementation should be a design choice
DPDK can be one of the options but should not be mandated to be the only one.
Technical challenges:
  Various <processor+ accelerator + profile> combinations possible for AAL implementation.
  One programming framework with specific features (e.g., DPDK’s memory management) may not be optimum for all.
Logistic challenges:
  API upstreaming & approval latency + Sync. between O-RAN spec. publication & DPDK release cadence.
  Not all vendors contributing to O-RAN AAL may be active members of DPDK.
Why not DPDK only?
Proposal 2:
AALI API definition should not dictate a specific implementation (e.g., DPDK) of AALI.

## Slide 5: AALI API beyond fec (1/6)
BBDEV API and inline API: Gap analysis
BBDEV API: General features
Developed for lookaside acceleration (FEC).
Provides programming framework for “FPGA and/or fixed function accelerators”.
Assumes DPDK based memory management – mempool & mbuf.
  Restriction:
    Mbuf supports fixed size area for packet data payload.
    Potential overallocation of memory, when packet size varies dynamically.
metadata
payload
metadata
payload
metadata
payload
mbuf0
mbuf1
mbuf2
…
Fig. 2 mbufs with fixed size within DPDK mempool

## Slide 6: AALI API beyond fec (2/6)
BBDEV API and inline API: Gap analysis
BBDEV API: Memory management (1/2)
DPDK based memory management – mempool & mbuf (contd.)
  Issue 1, RX side:
    Mbufs used to receive network packets are unpredictable in a multi-threaded environment.
    Application does not know in advance where packets will be received in the memory.
    Requires additional steps for packet reordering.
Fig. 3 Out-of-order packet reception in DPDK mempool

## Slide 7: AALI API beyond fec (3/6)
BBDEV API and inline API: Gap analysis
BBDEV API: Memory management (2/2)
DPDK based memory management – mempool & mbuf (contd.)
  Issue 2:
    DPDK RX/TX functions require CPU into the critical path.
    Can not use direct GPU <> NIC communication techniques (e.g., GPUDirect Async)
Fig. 4 CPU involvement in DPDK Rx function call
Proposal 3:
Memory management should be out of scope of AALI definition and left up to AALI implementation.

## Slide 8: AALI API beyond fec (4/6)
BBDEV API and inline API: Gap analysis
BBDEV API: Queue mapping
BBDEV API is centered around the notion of “Queue” for accelerator offload.
One enqueue call can offload work associated with a single “Queue ID”.
An AAL queue supports only one type of AAL profile.
  Inefficient for inline acceleration, where profiles are defined on a “per-channel” basis.
  Inline API invokes enqueue function “per-slot”, with workload combining multiple “per-channel” profiles.
  BBDEV API invokes separate enqueue functions for DL and UL workloads  inefficient for inline profile while accelerating workload for “S” slot.
Fig. 5 AAL Device with multiple queues as shown in AAL GAnP Spec.
Application
AAL DevID 1
Thread #0
Thread #1
QueueID0
QueueID1
Library|Driver
HW accelerator
Proposal 4:
AALI API shall provide flexibility for multi-profile workload launch in a single enqueue call.

## Slide 9: AALI API beyond fec (5/6)
BBDEV API and inline API: Gap analysis
BBDEV API: Device mapping
An AAL device maps to a single HW accelerator.
Application control to which device the workload will be launched to.
  Use case 1: when multiple accelerator devices are available supporting the same acceleration profile, application should not dictate workload distribution between the devices.
    Example: using high speed GPU interconnect NVLINK, large workload execution can be extended over multiple GPUs (without involving CPU in between).
  Use case 2: chaining of multiple profiles, supported by multiple accelerator devices.
    Example: appending “rest of the PHY” acceleration on device 2 with existing FEC acceleration on device 1. Device 1 and 2 should be able to communicate directly.
Fig. 6 AAL Device mapping with multiple devices as shown in AAL GAnP Spec.
Proposal 5:
AALI API shall provide flexibility for implementation-specific scheduling/distribution of workload across multiple HW accelerator devices.
Application
AAL Device 1
Api(devID1, queueID, …)
Library|Driver
HW accelerator
AAL Device 2
Library|Driver
HW accelerator
Api(devID2, queueID, …)

## Slide 10: AALI API beyond fec (6/6)
BBDEV API and inline API: Gap analysis
BBDEV API: Enqueue/Dequeue
Mapping of Queue centric enqueue/dequeue function to “multi-cell, multi-UE, multi-channel” workload is not straightforward.
“Queue ID” cannot be directly mapped to “Cell ID” and/or “UE ID” and/or “PHY channel type”.
  Why? : A single enqueue invocation can not combine workload from “multiple queues”.
  Alternate solution: Instead of a single Queue ID, use an array of Task IDs per enqueue call, to track progress of individual tasks (per cell/per UE/per channel), through potentially multiple dequeue calls (one per task, priority based).
ORAN_AAL_enqueue {
Task1:
CellA << PUSCH;
CellB << PUSCH;
Task2:
CellC << PDSCH;
...
Proposal 6:
AALI shall allow triggering of combined multi-cell/multi-UE/multi-PHY channel workload with a single invocation of enqueue function, using an array of “Task IDs”, instead of a single “Queue ID”.

## Slide 11: Conclusion
O-RAN shall define AALI API in terms of Requirement, AAL profiles, Operations and Information/data model.
AALI API definition should not be guided by a specific AALI implementation.
AALI API definition should not dictate a specific implementation (e.g., DPDK) of AALI.
Memory management should be out of scope of AALI definition and left up to AALI implementation.
AALI API shall provide flexibility for multi-profile workload launch in a single enqueue call.
AALI API shall provide flexibility for implementation-specific scheduling/distribution of workload across multiple HW accelerator devices.
AALI shall allow triggering of combined multi-cell/multi-UE/multi-PHY channel workload with a single invocation of enqueue function, using an array of “Task IDs”, instead of a single “Queue ID”.
Summary of Proposals