## Slide 1: AAL API for inline acceleration
Elena Agostini and Lopamudra Kundu (06/21/2021)

## Slide 2: agenda
AAL architecture for inline, L1-high PHY acceleration profile
AAL API header functions
  AAL_init
  AAL_config
  AAL_enqueue
  AAL_dequeue
  AAL_finalize

## Slide 3: Aal architecture for inline profile
For inline profile, Acceleration Abstraction Layer (AAL) interfaces between L1 application SW and L1 HW accelerator.
AAL interacts with HW accelerator through the following set of APIs:
  Initialize
  Configure
  Enqueue
  Dequeue
  Finalize
Application discovers HW accelerator’s capability prior to calling AAL APIs.
NIC
L2 + Application SW
HW accelerator (GPU)
Enqueue
Dequeue
Configure
Initialize
L2 <-> L1 interface (e.g., FAPI)
SW Libraries
(HW accel. vendor specific)
Accel. Driver (CUDA)
NIC Driver (MLNX_OFED)
User space Software
AAL
L1 application SW
Kernel space
Finalize

## Slide 4: AAL API - key functions

## Slide 5: AAL API function 1: Initialize
AAL_init
Function | AAL_init | 
Function prototype | int AAL_init (AAL_handler* AAL_h, struct context_config ctx_cfg); | 
Description | Create a new AAL L1 context [1] Associate AAL L1 context with the underlying HW accelerator (e.g., GPU) and NIC Configure AAL L1 context with parameters in ctx_cfg (may be implementation-specific) | 
Parameters | Type | Description
AAL_h | AAL_handler* | AAL handler pointer, indicating to the memory area where the AAL L1 context handler (AAL_h) will be stored
ctx_cfg | struct context_config | Structure containing set of parameters to configure the AAL L1 context, provided by the application
Return |  | 
Integer | 0 on success, Linux error code otherwise | 
[1] Analogous to the notion of “AAL LPU”

## Slide 6: Additional Details (AAL_init)
struct context_config {
// GPU id
int * gpu_ids;
// Network address PCIe bus address
std::string nic_bus_addr;
// Network card MTU
uint16_t nic_mtu;
// Implementation-specific configurations (example)
std::vector<struct cell_mplane_info> cell_mplane_list;
std::vector<uint8_t> ul_cores; // List of CPU cores for UL
std::vector<uint8_t> dl_cores; // List of CPU cores for UL
...
};
Example structure: context_config

## Slide 7: Aal api function 2: configure
AAL_config
Function | AAL_config | 
Function prototype | int AAL_config (AAL_handler AAL_h, struct cell_phy_params cell_cfg); | 
Description | This function configures AAL L1 context with a set of cell specific PHY static parameters AAL L1 context creates a number of cells based on the cell_cfg command | 
Parameters | Type | Description
AAL_h | AAL_handler | Context handler where to set cell PHY parameters
cell_cfg | struct cell_phy_params | Cell PHY (static) parameters
Return |  | 
Integer | 0 on success, Linux error code otherwise | 

## Slide 8: Additional details (AAL_config)
struct cell_phy_params {
uint16_t mplane_id; // used to match PHY params with M-plane params
uint16_t phyCellId; // physical cell Id
uint16_t nRxAnt; // number of receiving antennas
uint16_t nTxAnt; // number of transmitting antennas
uint16_t nPrbUlBwp; // number of PRBs allocated in UL BWP
uint16_t nPrbDlBwp; // number of PRBs allocated in DL BWP
uint8_t mu; // numerology [0-4]
float beta_dmrs; // DMRS amplitude scaling
float beta_qam; // QAM amplitude scaling
...
};
Example structure: cell_phy_params

## Slide 9: AAL API function 3: enqueue
AAL_enqueue
Function | AAL_enqueue | 
Function prototype | int AAL_enqueue (AAL_handler AAL_h, struct slot_command slot_cmd); | 
Description | Enqueue workload to AAL L1 context (created at AAL_h), with slot specific PHY channel parameters embedded in slot_cmd | 
Parameters | Type | Description
AAL_h | AAL_handler | Context handler that will process the list of cells and associated PHY channels
slot_cmd | struct slot_command { uint16_t task_id; cell_commands cells; } | (1) task_id : can be used to poll asynchronously the status of the enqueued workload (2) cells: list of cells to be processed in UL/DL, with an associated list of PHY channels and parameters (e.g., FAPI PDU) per cell
Return |  | 
Integer | 0 on success, Linux error code otherwise | 

## Slide 10: Additional details (AAL_enqueue)
struct phy_slot_params {
struct pusch_params * pusch;
struct pdsch_params * pdsch;
…
}; struct pusch_params {
uint32_t ue_tb_size[MAX_PUSCH_UE_PER_TTI];
PuschCellGrpDynPrm_t cell_grp_info;
PuschCellDynPrm_t cell_dyn_info;
PuschUeGrpPrm_t ue_grp_info[MAX_PUSCH_UE_GROUPS];
PuschDmrsPrm_t ue_dmrs_info[MAX_PUSCH_UE_PER_TTI];
…
// CPU buffer for data O/P, provided by the application
void * output_buffer;
};
struct slot_command {
// Identifier for this workload
uint16_t task_id;
// List of cells with PHY channels
struct cell_command * cells;
// Reference tick time
nanoseconds tick;
};
struct cell_command {
// 3GPP slot info
slot_info slot;
// List of channels per cell
phy_slot_params params;
};
Example structure: slot_command

## Slide 11: AAL API function 4: dequeue
AAL_dequeue
Function | AAL_dequeue | 
Function prototype | int AAL_dequeue (AAL_handler AAL_h, struct output_task * o_task); | 
Description | Polls L1 to get the status of an enqueued list of cells through the task_id stored in the o_task structure If the status is COMPLETE, the “o_task” is filled with output info. per cell | 
Parameters | Type | Description
AAL_h | AAL_handler | Context handler that has processed the list of cells and PHY channels
o_task | struct output_task * | Application should set the task_id in o_task to query the status of the workload associated with the list of cells enqueued in “AAL_enqueue” call
Return |  | 
Integer | 0 on success, Linux error code otherwise | 

## Slide 12: Additional details (AAL_dequeue)
struct output_task {
// Identifier to query workload status
uint16_t task_id; // populated by the application
// Status of the workload (ERROR, IN PROGRESS, DONE, …)
enum completion_status_type status; // populated by AAL implementation
};
Example structure: output_task

## Slide 13: AAL API function 5: finalize
AAL_finalize
Function | AAL_finalize | 
Function prototype | int AAL_finalize (AAL_handler AAL_h) | 
Description | Destroy the AAL L1 context, free resources, memory allocations and PCIe devices associated to that context | 
Parameters | Type | Description
AAL_h | AAL_handler | Context handler to be destroyed
Return |  | 
Integer | 0 on success, Linux error code otherwise | 

## Slide 14: proposals
Proposal 1: AAL common API will provide the following functionalities-
  AAL LPU initialization (AAL_init) and finalization (AAL_finalize)
  AAL LPU configuration (AAL_config)
Proposal 2: AAL profile specific API will provide the following functionalities-
  Profile specific workload enqueue (AAL_enqueue)
  Profile specific workload dequeue and/or workload processing status query (AAL_dequeue)
Proposal 3: For L1-high PHY inline acceleration, consider FAPI PDUs as the baseline for defining cell_config and slot_command structures for different PHY channels.